## Slide 1: Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty Mid-term Presentation Master Thesis
Chia-Ling Yang
Technical University Munich (TUM)
Chair of Production and Supply Chain Management
Prof. Dr. Martin Grunow
Superviosr: Bahar Okumusoglu
Munich, 23rd of September 2024

## Slide 2: Agenda
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
RL Fundamentals
Literature Review
Methodology
Implementation – Preliminary Result
Outlook

## Slide 3: Background

## Slide 4
Background
Problem Formulation
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Literature Review
…
Bouckaert et al. (2021) "Net zero by 2050: A roadmap for the global energy sector."
Renewable Energy Integration
Low Carbon Emission Transportation
RL Fundamental
Outlook
Notes: A roadmap for global energy sector proposed by International Energy Agency

## Slide 5: “Security- and Human-centered Energy Transition”
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Extreme Weather
Energy Demand
IEA (2023). “World Energy Outlook 2023” https://www.iea.org/reports/world-energy-outlook-2023
Renewable Energy Integration
Low Carbon Emission Transportation
Fast Charging
High Uncertainty
Decentralization
Rising Importance of Distribution System/Network Operator (DSO)
Instability of Distribution Network
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook
Notes: Who cares about the problem? Why is the problem important for them?
Important for DSO
If not carefully taken care: cascading failure, prompt break down

## Slide 6: Problem Formulation

## Slide 7
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
OPF
Generation
Battery
Load
DSO
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook

## Slide 8: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
Set and index
Decision variable

## Slide 9: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Parameters
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook

## Slide 10: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Objective Function – Generation cost minimization
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook

## Slide 11: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Constraints
(3) Active power balance at nodes
(4) Reactive power balance at nodes
(2) Reactive power calculation of lines
(1) Active power calculation of lines
(5) Voltage limitation at nodes
(6) Active power generation limitation
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook

## Slide 12: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Constraints
(7) Reactive power generation limitation
(8) Apparent power (line load) limitation
(9) Phase angle limitation
(10) Energy balance of EV charging
(11) State of charge (SOC) limitation
(12) Charging limitation
(13) Discharging limitation
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook

## Slide 13: Reinforcement Learning (RL) provides potentials to tackle the non-convex, non-linear OPF problem with high uncertainty in the real world.
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Solving OPF is challenging
Non-convexity
Non-Linearity
Uncertainty
RL is a promising
Robustness
Fast online implementation
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook
Notes: For fast online implementation: Current requirement: 15 min and in the future it might decrease due to the introduction of real time pricing.

## Slide 14: Reinforcement Learning Fundamental

## Slide 15: Markov Decision Process
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Environment
Agent
 | state
 | action
 | transition prob. dist.
 | reward
 | policy
 | state
 | action
 | transition prob. dist.
 | reward
 | policy
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook

## Slide 16: Actor-Critic Framework
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Actor
Critic
Environment
; | current state; next state
 | action
 | reward
 | policy
 | value function
 | number of sampled experiences
 | advantage function
 | value estimation of taking action
 | current state; next state
 | action
 | reward
 | policy
 | value function
 | number of sampled experiences
 | advantage function
 | value estimation of taking action
Actor
Actor
Critic
Critic
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook
Notes: Categories: value-based (Q-learning), policy-based(Reinforce) and hybrid(A-C)
A-C is preferred in our use case since it handles continuous action space better and at the same time it is more stable.

## Slide 17: Common RL Algorithms
Massaoudi, M. S., Abu-Rub, H., & Ghrayeb, A. (2023). Navigating the landscape of deep reinforcement learning for power system stability control: A review. IEEE Access, 11, 134298-134317.
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook

## Slide 18: Literature Review

## Slide 19
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Title | Author | Journal | Year | Methodology | EV | RL | Without DC Approximation
The Promise of EV-Aware Multi-Period OPF Problem: Cost and Emission Benefits | Kayacık et al. | Sustainable Energy, Grids and Networks | 2023 | Second-Order Cone Programming (SOCP) | X |  | 
Symbiotic organisms search algorithm-based security-constrained AC–DC OPF regarding uncertainty of wind, PV and PEV systems | Duman et al. | Soft Computing | 2021 | Heuristic: Symbiotic Organisms Search | X |  | 
Optimal charging of electric vehicles in smart grid: Characterization and valley-filling algorithms | Chen et al. | 2012 IEEE SmartGridComm | 2012 | Heuristic: Valley-Filling Algorithm | X |  | 
Real-Time Optimal Power Flow: A "Lagrangian" Based Deep Reinforcement Learning Approach | Yan and Xu | IEEE Transactions on Power Systems | 2020 | Deep Deterministic Policy Gradient |  | X | 
A Data-driven Method for Fast AC Optimal Power Flow Solutions via Deep Reinforcement Learning | Zhou et al. | Journal of Modern Power Systems and Clean Energy | 2020 | Proximal Policy Optimization (PPO) |  | X | 
Feasibility Constrained Online Calculation for Real-Time Optimal Power Flow: A Convex Constrained Deep Reinforcement Learning Approach | Sayed et al. | IEEE Transactions on Power Systems | 2023 | Soft Actor-Critic |  | X | 
Network-Constrained Reinforcement Learning for Optimal EV Charging Control | Wu et al. | 2023 IEEE SmartGridComm | 2023 | Twin Delayed Deep Deterministic Policy Gradient (TD3) | X | X | 
This work |  |  |  | PPO | X | X | X
Background
Problem Formulation
Literature Review
…
RL Fundamental
Outlook

## Slide 20: Methodology

## Slide 21: Critical Components in RL – States and Actions
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Grid network settings
EV driving demands
Power generation capacity
Power consumption
EV state of charge
Power flow solver …
Environment
States
Active power generation output
Reactive power generation output
Charging/Discharging power for EV
Agent
Actions
Background
Problem Formulation
Methodology
Implementation
…
Outlook
Notes: ### \(P_g\) and \(V_g\) as Actions:
- **Traditional Approach:** Many OPF formulations use \(P_g\) and \(V_g\) (generator voltage magnitudes) as control variables.
- **Advantages:** Voltage control through \(V_g\) directly affects reactive power flows and voltage stability in the grid.
- **Challenges:** Requires the RL agent to learn how voltage adjustments impact power flows, which may increase complexity.
### \(P_g\) and \(Q_g\) as Actions:
- **Alternative Approach:** By setting both active power (\(P_g\)) and reactive power (\(Q_g\)) as actions, you give direct control over both.
- **Advantages:** This simplifies the RL agent's task of balancing power generation and reactive power, potentially making learning more intuitive since \(Q_g\) directly affects voltage levels.
- **Challenges:** The relationship between \(Q_g\) and voltage magnitudes is non-linear, so the RL agent needs to indirectly control voltage through \(Q_g\).
In short, using \(P_g\) and \(Q_g\) as actions is a valid and potentially more intuitive approach, especially if the goal is to focus on directly controlling both active and reactive power flows in the grid. However, it may lead to different challenges in terms of the RL agent's learning process and the dynamics of how voltage is controlled.

## Slide 22: Critical Components in RL – Reward Function
< 0 penalty from power flow divergence
< 0 penalty from line load violation
< 0 penalty from voltage violation
< 0 penalty from phase angle violation
< 0 penalty when SOC goes below a certain point
>0 reward when no divergence and violation
>0 generation cost
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Methodology
Implementation
…
Outlook

## Slide 23: Proximal Policy Optimization
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Schulman, J., Wolski, F., Dhariwal, P., Radford, A., & Klimov, O. (2017). Proximal policy optimization algorithms. arXiv preprint arXiv:1707.06347.
where
: estimated advantage function
: small hyperparameter
Conservative updating!
Background
Problem Formulation
Methodology
Implementation
…
Outlook
Notes: PPO was developed by John Schulman in 2017,[1] and had become the default reinforcement learning algorithm at OpenAI. Many experts called PPO the state of the art because it seems to strike a balance between performance and comprehension. Compared with other algorithms, the three main advantages of PPO are simplicity, stability, and sample efficiency.  suits my situation perfectly since I do not own a data center.

## Slide 24: Implementation - Training

## Slide 25: Assumptions
The position of slack/reference bus does not change.
There is an EV group at each load bus.
The number of EV in a group is the integer of the mean of active power at loads
The EVs at the same bus have the same battery capacity and the same driving demands.
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Methodology
Implementation
…
Outlook
Active power and reactive power of loads are randomly sampled with standard deviation =1.
Active power generation capacity is uniformly distributed between max. and min.
EV driving profile data comes from emobpy. [Gaete-Morales, C., Kramer, H., Schill, WP. et al. An open tool for creating battery-electric vehicle time series from empirical data, emobpy. Sci Data 8, 152 (2021). https://doi.org/10.1038/s41597-021-00932-9]
Data Sample

## Slide 26: Test Case – IEEE 14 Bus System
Slack/Reference
Generator
Load
Background
Problem Formulation
Methodology
Implementation
…
Outlook

## Slide 27: Training Performance
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Methodology
Implementation
…
Outlook
Expected reward per episode

## Slide 28: Outlook

## Slide 29: Evaluation of the RL model
Selecting a mathematical optimization method as benchmark
Second-order conic programming
More different test cases
        IEEE Case 9
        IEEE Case 30
        and more…
Background
Problem Formulation
Methodology
Implementation
…
Outlook

## Slide 30: Q&A