## Slide 1: Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty Mid-term Presentation Master Thesis
Chia-Ling Yang
Technical University Munich (TUM)
Chair of Production and Supply Chain Management
Prof. Dr. Martin Grunow
Superviosr: Bahar Okumusoglu
Munich, th of September 2024

## Slide 2: Agenda
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
RL Fundamentals
Literature Review
Methodology
Implementation – Preliminary Result
Outlook

## Slide 3: Background

## Slide 4
Background
Problem Formulation
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Literature Review
Methodology
Outlook
Bouckaert et al. (2021) "Net zero by 2050: A roadmap for the global energy sector."
Renewable Energy Integration
Low Carbon Emission Transportation
Notes: A roadmap for global energy sector proposed by International Energy Agency

## Slide 5: “Security- and Human-centered Energy Transition”
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
Extreme Weather
Energy Demand
IEA (2023). “World Energy Outlook 2023” https://www.iea.org/reports/world-energy-outlook-2023
Renewable Energy Integration
Low Carbon Emission Transportation
Fast Charging
High Uncertainty
Decentralization
Rising Importance of Distribution System/Network Operator (DSO)
Instability of Distribution Network
Notes: Who cares about the problem? Why is the problem important for them?
Important for DSO
If not carefully taken care: cascading failure, prompt break down

## Slide 6: Problem Formulation

## Slide 7
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
OPF
Generation
Battery
Load
DSO

## Slide 8: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
Set and index
Decision variable

## Slide 9: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
Parameters

## Slide 10: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
Objective Function

## Slide 11: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
Constraints
Active power balance at nodes
Reactive power balance at nodes
Reactive power calculation of lines
Active power calculation of lines
Voltage limitation at nodes
Active power generation limitation

## Slide 12: Optimal Power Flow
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
Constraints
Reactive power generation limitation
Apparent power (line load) limitation
Phase angle limitation
Energy balance of EV charging
State of charge (SOC) limitation
Charging limitation
Discharging limitation

## Slide 13: Reinforcement Learning (RL) provides potentials to tackle the non-convex, non-linear OPF problem with high uncertainty in the real world.
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
Solving OPF is challenging
Non-convexity
Non-Linearity
Uncertainty
RL is a promising
Robustness
Fast implementation online

## Slide 15: Markov Decision Process
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Environment
Agent
 | state
 | action
 | transition prob. dist.
 | reward
 | policy
 | state
 | action
 | transition prob. dist.
 | reward
 | policy

## Slide 16: Actor-Critic Framework
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Actor
Critic
Environment
; | current state; next state
 | action
 | reward
 | policy
 | value function
 | number of sampled experiences
 | advantage function
 | value estimation of taking action
 | current state; next state
 | action
 | reward
 | policy
 | value function
 | number of sampled experiences
 | advantage function
 | value estimation of taking action
Actor
Actor
Critic
Critic
Notes: Categories: value-based (Q-learning), policy-based(Reinforce) and hybrid(A-C)
A-C is preferred in our use case since it handles continuous action space better and at the same time it is more stable.

## Slide 17: Common RL Algorithms
Massaoudi, M. S., Abu-Rub, H., & Ghrayeb, A. (2023). Navigating the landscape of deep reinforcement learning for power system stability control: A review. IEEE Access, 11, 134298-134317.
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty

## Slide 18: Literature Review

## Slide 19
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Background
Problem Formulation
Literature Review
Methodology
Outlook
Title | Author | Journal | Year | Methodology | EV | RL | Without DC Approximation
The Promise of EV-Aware Multi-Period OPF Problem: Cost and Emission Benefits | Kayacık et al. | Sustainable Energy, Grids and Networks | 2023 | Second-Order Cone Programming (SOCP) | X |  | 
Symbiotic organisms search algorithm-based security-constrained AC–DC OPF regarding uncertainty of wind, PV and PEV systems | Duman et al. | Soft Computing | 2021 | Heuristic: Symbiotic Organisms Search | X |  | 
Optimal charging of electric vehicles in smart grid: Characterization and valley-filling algorithms | Chen et al. | 2012 IEEE SmartGridComm | 2012 | Heuristic: Valley-Filling Algorithm | X |  | 
Real-Time Optimal Power Flow: A "Lagrangian" Based Deep Reinforcement Learning Approach | Yan and Xu | IEEE Transactions on Power Systems | 2020 | Deep Deterministic Policy Gradient |  | X | 
A Data-driven Method for Fast AC Optimal Power Flow Solutions via Deep Reinforcement Learning | Zhou et al. | Journal of Modern Power Systems and Clean Energy | 2020 | Proximal Policy Optimization (PPO) |  | X | 
Feasibility Constrained Online Calculation for Real-Time Optimal Power Flow: A Convex Constrained Deep Reinforcement Learning Approach | Sayed et al. | IEEE Transactions on Power Systems | 2023 | Soft Actor-Critic |  | X | 
Network-Constrained Reinforcement Learning for Optimal EV Charging Control | Wu et al. | 2023 IEEE SmartGridComm | 2023 | Twin Delayed Deep Deterministic Policy Gradient (TD3) | X | X | 
This work |  |  |  | PPO | X | X | X

## Slide 20: Methodology

## Slide 21: Critical Components in RL
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Grid network settings
EV driving demands
Power generation capacity
Power consumption
EV state of charge
Power flow solver …
Environment
States
Active power generation output
Reactive power generation output
Charging/Discharging power
Agent
Actions
when power flow diverges
when line violation occurs
when voltage violation occurs
when SOC goes below a certain point
when no divergence and violation
Reward

## Slide 22: Reward Function

## Slide 23: Proximal Policy Optimization
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty
Schulman, J., Wolski, F., Dhariwal, P., Radford, A., & Klimov, O. (2017). Proximal policy optimization algorithms. arXiv preprint arXiv:1707.06347.
where
: estimated advantage function
: small hyperparameter
Conservative updating!
Notes: PPO was developed by John Schulman in 2017,[1] and had become the default reinforcement learning algorithm at OpenAI. Many experts called PPO the state of the art because it seems to strike a balance between performance and comprehension. Compared with other algorithms, the three main advantages of PPO are simplicity, stability, and sample efficiency.  suits my situation perfectly since I do not own a data center.

## Slide 24: Implementation - Training

## Slide 25: Assumptions
Loads and maximum generation are randomly sampled during training.
All EVs exist at the load buses. The EVs at the same buses have the same battery capacity and the same driving demands.
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty

## Slide 26: Training Performance
Chia-Ling Yang | Exploring Reinforcement Learning Solutions for EV-aware Optimal Power Flow Under Uncertainty

## Slide 27: Outlook

## Slide 28
Benchmark: Math. Optimization Method
Test on more different test cases

## Slide 29: Q&A